## Slide 1: SYNFLOW - A Success Story Walter Leitner
Center for Molecular Transformation @RWTH Aachen (Dr. Stefan Palkovits, Cora Schings)
DECHEMA (Dr. Alexis Bazzanella)

## Slide 2: Chemical and Pharmaceutical Industry
Importance of the chemical and pharmaceutical industry in Europe |  | 
European Chemical Industry | Employment | 1,19 Million direct jobs*
 | Chemicals sales | 558 billion €** 17.8% world market share
European Pharmaceutical Industry | Employment | 700.000 direct jobs***
 | Pharmaceuticals sales | 160 billion € *** 26.7% of world sales
* Eurostat 2012
** Cefic Chemdata International 2013 *** European Federation of Pharmaceutical Industries, Key-data 2012

## Slide 3
The Material Supply Chain: A ChemisTree
function
nutrition
> 105 products
~ 102 intermediats
~ 101 basic chemicals
100 petroleum
care
health
alternative carbon ressources
sustainable synthetic pathways and processes
new or improved products

## Slide 4: The Green Chemistry Challenge
E- Factor = m(waste)/m(product) (R. Sheldon, 1993)
Petrochemistry
Basic Chemicals
Fine Chemistry
Pharaceuticals
kg waste/kg product
R. Sheldon, Green Chemistry, 2007, 9, 1273-1283

## Slide 5: Catalysis: A Key Technology
>90% of new chemical processes
13 billion $ catalyst market
>1,000 billion $ value generation
15-20% of the total economy
2001: Asymmetric Catalysis (Sharpless, Knowles, Noyori)
2005: Olefin Metathesis (Chauvin, Grubbs, Schrock)
2007: Surface Science (Ertl)
2010: Pd-Catalyzed C-C Coupling (Heck, Negishi, Suzuki)

## Slide 6: The SYNFLOW Concept
batch-wise
large volume
high E-factors
many unit operations
low space time yields
labour intensive
molecular
AND
engineering
sciences
continuous-flow
small and flexible
no VOC, no waste
integrated process
high space time yield
largely automated

## Slide 7: The SYNFLOW Consortium
20 partners from 8 European countries
Coordination: CMT@RWTH Aachen
Management: Dechema
16,6 Mio € budget / 11 Mio € EU funding
September 1, 2010 – August 31, 2014

## Slide 8: Research Programme: Work Packages & Case Studies
Integrated & Interdisciplinary Approach
Directed to new methodologies
Robust and generic processes
Based on industrial case studies
Aimed at demonstration (kg/d)

## Slide 9
scCO2
scCO2
Supported Ionic Liquid
Phase
H2
U. Hintermair, G. Franciò, W. Leitner, Chem. Eur. J. 2013, 19, 4538 – 4547.
Notes: ONE example for the approaches taken,
Exemplified for asymmetric hydrogenation as „case study“ because of ist broad utility in pharma !
Start with FLOW SCHEME, scCO2 combines DISTILLATION and EXTRACTION (Destraction, Zosel) => SUBSTRATES / PRODUCTS for Pharma!
NO organic solvent, PURE product without any further purification directly obtained.
CATALYST retained in SILP material: complex is IN SOLUTION, but material is free flowing POWDER !
Molecular structure and environment (IL, support) sontrol the performance! Further optimization possible!
STY = Reactor of 1 L volume (MASSKRUG !!) can produce 0.3 x 24 x 365 = 2628 kg product, i.e. ca 1 t of product per year !

## Slide 10
scCO2
scCO2
Supported Ionic Liquid
Phase
H2
Notes: ONE example for the approaches taken,
Exemplified for asymmetric hydrogenation as „case study“ because of ist broad utility in pharma !
Start with FLOW SCHEME, scCO2 combines DISTILLATION and EXTRACTION (Destraction, Zosel) => SUBSTRATES / PRODUCTS for Pharma!
NO organic solvent, PURE product without any further purification directly obtained.
CATALYST retained in SILP material: complex is IN SOLUTION, but material is free flowing POWDER !
Molecular structure and environment (IL, support) sontrol the performance! Further optimization possible!
STY = Reactor of 1 L volume (MASSKRUG !!) can produce 0.3 x 24 x 365 = 2628 kg product, i.e. ca 1 t of product per year !

## Slide 11: The SYNFLOW Deliverables: Demonstrators
Buchwald-Hartwig
(AZ/BTS/Invite)
Hydrogenation
(AZ/RWTH Aachen)
Olefin Telomerization
(Evonik/Erlangen)

## Slide 12: The SYNFLOW Deliverables: Key Criteria
Effective catalyst
Product quality
Downstream processing
Energy & Solvents
Timelines for scale-up
Flexibility / Scope
Commercialisation of new catalyst for Buchwald Hartwig amination
Reduced metal contamination
Patents on new reactor technologies
Energy: -15%, up to -50% E-factor: reduced up to 10x
Reduced by 25%
Drug development projects up to 100 Mios €

## Slide 13: The SYNFLOW Legacy
26 publications in peer-reviewed journals
12 keynotes at international conferences
9 Postdocs / 36 PhD students
Consortium Meeting, Tarragona, April 2011

## Slide 14: SYNFLOW dissemination activities
ACHEMA 2012
Joint Exhibition Booth
Conference Sessions Green solvents 2012
CHISA 2012
15th International Congress on Catalysis
Website: www.synflow.eu Twitter: @synflow_project
SYNFLOW
case studies
SYNFLOW
video

## Slide 15: The SYNFLOW Legacy
Synflow F3 Factory PolyCat
Marie-Curie ITN
Marie-Curie ITN
NRW / Ziel 2

## Slide 16: The SYNFLOW Legacy: Where to go next?
> improving known synthetic methods => novel synthetic pathways
> automated reactors => self-optimizing / adaptable reactors
> small and flexible units => novel operating windows
> pharmaceutical industry => cross-sectorial impact

## Slide 17: THANK YOU !!
πάντα ῥεῖ
panta rhei
„all flows“
Ἡράκλειτος
Heraclitus
ca 535 - 475 AD