## Slide 1: SteamBio
Flexible Superheated Steam Torrefaction and Grinding of Indigenous Biomass from Remote Rural Sources to Produce Stable Densified Feedstocks for Chemical and Energy Applications
Siegfried Egner
Fraunhofer Institute for Interfacial Engineering and Biotechnology IGB

## Slide 2: Outline
The Consortium
Fossil vs. renewable biomass
    Status quo
    Our vision
SteamBio
    Objectives
    On-site operation
    Downstream processing
  The SteamBio Business
    Supply chain

## Slide 3: The Consortium
The research leading to these results receives funding from the European Union’s Research and Innovation Programme Horizon 2020 under Grant Agreement No 636865.

## Slide 4: Outline
The Consortium
Fossil vs. renewable biomass
    Status quo
    Our vision
SteamBio
    Objectives
    On-site operation
    Downstream processing
  The SteamBio Business
    Supply chain

## Slide 5: Bioeconomy
Substitution of fossil carbon feedstock by renewable biomass
Lignocellulosic biomass is the biggest source of carbon
Alternative fuel for power plants
Green chemical building blocks

## Slide 6
Supply of fossil hydrocarbons via trans-European pipeline networks
Status quo

## Slide 7: Major locations of petrochemical sites in Europe
concentrated in
certain regions
heavily dependent on
fossil hydrocarbons
Petrochemical industry is

## Slide 8: Status quo – Supply of oil and gas in Europe
Established supply of fossil hydrocarbons by trans-European oil and gas pipelines

## Slide 9
Supply of renewable hydrocarbons out of lignocellulose from forestry via trans-European transportation networks
Our vision

## Slide 10: Sources of lignocellulosic biomass across Europe
0 – 10
11 – 25
26 – 50
51 – 75
76 – 100
Forest % share of land area

## Slide 11: Mismatch between locations of source and demand
0 – 10
11 – 25
26 – 50
51 – 75
76 – 100
Forest % share of land area
Urgent need of efficient trans-European delivery of biomass to chemical sites
Main forestry zones in remote areas
Chemical sites

## Slide 12: Challenges in handling lignocellulosic biomass
Solid material
Bulky feedstock with large particle size
High moisture content
No pipelining possible
Energy-intensive shredding for further use
Inefficient transportation
SteamBio – Mobile advanced torrefaction process
Minimization of transportation expenses by pretreatment of biomass
Our concept

## Slide 13
Residues / Pruning / Thinning / Chips
Process “A“
Process “B“
Process “C“
solids
liquids
gas
SteamBio – Superheated steam torrefaction of lignocellulosic biomass

## Slide 14: Outline
The Consortium
Fossil vs. renewable biomass
    Status quo
    Our vision
SteamBio
    Objectives
    On-site operation
    Downstream processing
  The SteamBio Business
    Supply chain

## Slide 15
Definition of optimum SHS processing parameters for assorted agro-forestry residues
Facilitation of transportation and storage of the torrefied outputs
Develop and build of mobile SteamBio system on a trailer as a scalable demonstrator unit
Process six different biomass materials with confirmation of stability of the output for over 12 month
Demonstration of the SteamBio process at over five different locations
Validate the technical and economic viability of the integrated process
Confirm the full life economic, environmental and social sustainability of the entire approach
SteamBio – Objectives

## Slide 16
On-site operation
Superheated steam (SHS) processing
Combined milling in SHS atmosphere
Pre- and post-handling systems (coveying, filling, loading, packaging, etc.)
Volatiles fractionation (e.g. selective condensation)
Downstream processing
Organosolv-process
High-vacuum and flash distillation
Liquid-liquid extraction
SteamBio – Enabling technologies

## Slide 17: SHS processing so far just used for drying
Superior heat transfer properties compared to hot air
Reduced processing time and lower specific energy consumption
No oxidative reactions and avoiding the risk of fire or explosions
Allowing recovery of energy and volatile compounds

## Slide 18: The SteamBio SHS torrefaction process
Increase in energy density of the solid biomass
Decrease in volumetric density of the solid biomass
Reduction in power consumption required for grinding
Improved transport and storage stability
SHS processing extended operation

## Slide 19
E.g. organosolv-process
Downstream processing – Solid handling

## Slide 20
E.g. extraction column with distillation recovery
Downstream processing – Liquid (condensable) handling

## Slide 21: Outline
The Consortium
Fossil vs. renewable biomass
    Status quo
    Our vision
SteamBio
    Objectives
    On-site operation
    Downstream processing
  The SteamBio Business
    Supply chain

## Slide 22: Supply chain level 1 – Local pretreatment
S
N
FIN
Local forestry
districts
Mobile SteamBio-service of pretreatment
101 km

## Slide 23
S
N
FIN
Supply chain level 2 – Short distance transportation
FIN
S
N
Mobile SteamBio-service of pretreatment
Shipping
terminals
102 km

## Slide 24
FIN
S
N
Shipping
terminals
Chemical process
sites
103 km
Supply chain level 3 – Trans-European transportation

## Slide 25: Thanks for Your Attention!
Coordination and Contact:
Siegfried Egner , Dipl.-Ing.
Fraunhofer Institute for Interfacial Engineering and Biotechnology IGB
Department of Physical Process Technology
Nobelstrasse 12, 70569 Stuttgart, Germany
Phone +49 711 970-3643 | Fax +49 711 970-3997
siegfried.egner@igb.fraunhofer.de
www.igb.fraunhofer.de